Track Construction Instructions

Next class we will be making measurements about centripetal acceleration using the marble roller coaster that you construct today. Follow the instructions and look at the example.

- Each group needs one template page.

- Cut length-wise along the dotted line.

- Fold each of the four sections inward along the solid lines to make four U-shaped tracks.

- On the two tracks labeled “CURVED TRACK” make small cuts in the sides of the track along the dotted lines.

- To curve the tracks, overlap tab A and tab B about 2 millimeters and then tape the two together. Now overlap tab C with tab B and tape them together. Next overlap tab D with tab C and tape them together.

Hints: 	a. Try to always overlap the tabs by the same amount. You want to make

an even curve.

b. Use as little tape a possible. We will roll a marble down the track and

it needs to be as smooth as possible.

c. It will be much easier to tape all of one side before doing the other

side.

- Overlap the two curved sections and tape them together to create one full loop.

- Tape the straight tracks together and then tape them to one end of the loop.

- Name your roller coaster something awesome and write it on one side of the straight track. Put both partner names on the other side.